## Slide 1
TEXAS LOW-LEVEL RADIOACTIVE WASTE
DISPOSAL COMPACT COMMISSION
Public Education Workshop
Commission Perspective: How the Compact Works
Brandon Hurley, Chair • John Salsman, Vice Chair • Linda Morris, Commissioner • Stephen Raines, Executive Director
Thursday, October 8, 2026 • Knoxville, Tennessee

## Slide 2
What We'll Cover
Part 1 — The Compact
The Compact: what it is and why it exists
What counts as low-level radioactive waste
TLLRWDCC's rules and recent rule changes
Preserving capacity for in-compact generators
Public comment periods & shipment limits
Part 2 — Generators & Brokers
What's in an import application (and top mistakes)
Generators, brokers, and the “last beneficial user”
Self-generated waste, irradiated hardware & international waste
Special programs: OSRP and SCATR
TLLRWDCC Public Education Workshop
2

## Slide 3
PART 1 — THE COMPACT
What Is Low-Level Radioactive Waste?
Federal definition (42 U.S.C. § 2021b(9))
Radioactive material that is not high-level radioactive waste, spent nuclear fuel, or by-product material.
Texas definition (Health & Safety Code Ch. 401)
Discarded or unwanted radioactive material, not exempted by DSHS rule
Meets the definition of “waste” under 10 C.F.R. § 61.2
Subject to concentration limits (10 C.F.R. § 61.55) and applicable disposal criteria
TLLRWDCC Public Education Workshop
3

## Slide 4
PART 1 — THE COMPACT
What LLRW Is Not — NORM & NARM
Excluded from “LLRW”
High-level radioactive waste (10 C.F.R. § 60.2)
Spent nuclear fuel (10 C.F.R. § 72.3)
By-product material (Health & Safety Code § 401.003(3)(B))
Naturally occurring radioactive material (non oil & gas)
Oil and gas NORM waste
NARM
Naturally occurring or accelerator-produced radioactive material — defined by DSHS rule as any such material except source or special nuclear material.
The Commission has no regulatory authority over NARM — it is not LLRW under statute.
TLLRWDCC Public Education Workshop
4

## Slide 5
PART 1 — THE COMPACT
What Is a Compact?
An agreement between two or more states to jointly manage low-level radioactive waste disposal — safely, efficiently, and with public health and safety as the priority. Every compact is approved by its member states and authorized by the U.S. Congress.
2
Party states: Texas (host) and Vermont
1998
Congress consented via Public Law 105–236
Texas is one of several regional compacts nationwide — each covering a group of member states that share a disposal facility.
TEXAS
Host state
VERMONT
Party state
Both states share one disposal facility and one set of rules — the Compact Waste Facility in Andrews County, Texas.
TLLRWDCC Public Education Workshop
5

## Slide 6
PART 1 — THE COMPACT
The Role of the Compact
Congress authorized and encouraged Texas and Vermont to efficiently manage and dispose of low-level radioactive waste, pursuant to the Low-Level Radioactive Waste Policy Act. Its goals:
1
Protect
Health, safety, and welfare of citizens and the environment
2
Enable
Economical management and disposal of low-level radioactive waste
3
Limit
The number of facilities needed to manage waste effectively
4
Reduce
Encourage the reduction of waste generation
5
Distribute
Costs, benefits, and obligations among the party states
TLLRWDCC Public Education Workshop
6

## Slide 7
PART 1 — THE COMPACT
How Do Compacts Interact With One Another?
Authorize movement
Agreements and authorizations let waste move between compacts and states.
Cooperate & respect rules
Party states manage waste within their borders and honor each compact's rules.
Share research & dialogue
Commissions research disposal practices and meet regularly through the Low-Level Forum.
Recommend & prepare
Commissions can recommend regulations, prepare contingency plans, and enter temporary emergency-disposal agreements.
TLLRWDCC Public Education Workshop
7

## Slide 8
PART 1 — THE COMPACT
TLLRWDCC Rules at a Glance
31 TAC 675.1
1995–2045 Waste Disposal Volume Estimate
31 TAC 675.20
Definitions
31 TAC 675.21
Exportation of Waste for Disposal
31 TAC 675.22
Export of Waste for Processing and Return for Disposal
31 TAC 675.23
Importation of Waste for Disposal
31 TAC 675.24
Exportation and Importation of Waste (Management Rule)
31 TAC 675.25
Capacity Reservation for Small Quantity Generators
TLLRWDCC Public Education Workshop
8

## Slide 9
PART 1 — THE COMPACT • NEW TOPIC
Recent & Upcoming Rule Changes
Management Rule (§ 675.24) Revision
The 2018 Management Rule requires reporting — not approval — for certain LLRW imported for management or disposal outside the Compact Waste Facility
Applies only in the host state (Texas)
TLLRWDCC is revising the rule to more clearly answer: if LLRW enters Texas and isn't going to the CWF, where is it going?
Recent Changes to the Import Application
Added “Current Location of Waste” — so the Commission knows whether waste has entered the Compact or is still being gathered or processed
Added a required affidavit to reinforce accuracy and truthfulness in applicant reporting
Added a question on the number of shipments requested
When an applicant submits an import application through the portal, TCEQ receives a copy
TLLRWDCC Public Education Workshop
9

## Slide 10
PART 1 — THE COMPACT
Preserving Capacity for In-Compact Generators
As host state, Texas has a legal obligation to provide disposal options for waste generated within Texas and Vermont — ensuring equitable access while managing volume and maintaining safety standards.
The Commission's Capacity Committee works to ensure adequate space remains available for in-compact generators.
Why It Matters
Protects long-term access for Texas and Vermont generators
Balances imports against remaining licensed capacity
Reviewed on an ongoing basis by the Capacity Committee
TLLRWDCC Public Education Workshop
10

## Slide 11
PART 1 — THE COMPACT
Public Comment Periods
Importation — 35 Days
Before approving waste to enter the Compact, a 35-day public comment period allows significant public input and transparency on potential environmental and health impacts. Adopted by rule (31 TAC § 675.23) in 2012.
Exportation — 15 Days
Approval to export waste out of the Compact requires a shorter, 15-day public comment period. Adopted by rule (31 TAC § 675.21) in 2022.
Emergency exports may be handled under separate exception procedures.
TLLRWDCC Public Education Workshop
11

## Slide 12
PART 1 — THE COMPACT • NEW TOPIC
How Many Shipments Are Allowed?
The Commission has set a general limit of 12 shipments per agreement for brokers and waste processors. A shipment is defined as a commitment to move a defined amount of waste into the state and is not tied to a single transportation action. Limitations on shipments are now included in agreement language.
275,000
Curie cap per fiscal year, set by the Texas Legislature (statute)
No Cap for Generators
Generators of waste have no limit on the number of shipments.
Related control point
Shipments above 15,000 curies require a curie release letter, requested in writing at least 15 days before shipment (see Conditional & Release Letters).
TLLRWDCC Public Education Workshop
12

## Slide 13
PART 1 — THE COMPACT
What's In an Import Application?
Applicant Info
Entity, contact, address, website
Generator Type
Generator, broker, processor, or collector — and small quantity generator status
Agreement Period
Fiscal year: September 1 – August 31
Waste Details
Volume, curies, class (A/B/C), form, sealed sources, origin, current location
Compliance
Any unresolved violations, complaints, or unpaid fees — with TLLRWDCC or other regulators
Certifications & Signatory
Accuracy, non-international origin, authorized signer, and an affidavit
TLLRWDCC Public Education Workshop
13

## Slide 14
PART 1 — THE COMPACT
Top 5 Errors on Import Petition Applications
1
Checking the “Small Quantity Generator” box improperly
2
Incorrect or missing information on the origin of the waste
3
Not including all waste streams
4
Typographical errors in waste volume and/or radioactivity
5
Not including the current location of the waste
TLLRWDCC Public Education Workshop
14

## Slide 15
PART 1 — THE COMPACT
Agreements — and When They Aren't Needed
What's In an Agreement
A contract authorizing importation of LLRW for disposal
Representations and warranties on how waste will be shipped
Possible revocation or suspension for non-compliance
Conditions on origin, waste type, volume, activity, and source
Stays in effect for its stated term unless amended or revoked
No fees — TLLRWDCC is funded by the Texas Legislature
No Application Needed When…
Radioactive material is transferred within Texas for treatment
Waste from inside the Compact (Texas or Vermont) is sent to WCS for disposal
Very low-level Class A waste is sent to WCS's RCRA facility
TLLRWDCC Public Education Workshop
15

## Slide 16
PART 1 — THE COMPACT • NEW TOPIC
Irradiated Hardware
Irradiated hardware importation requests must be submitted on a separate Importation Form from other waste streams.
15,000+
Curies triggers conditional-basis review
Requests for over 15,000 curies, if approved, are entered into on a conditional basis. See the Curie Limit Policy Paper for details on importation requests above this threshold.
Delivery requirement
All import applications and supplements/amendments must go to TLLRWDCC, WCS, and TCEQ by electronic mail. The Commission removed the requirement to provide hard copies to TCEQ and WCS. This change became effective on September 1, 2026.
TLLRWDCC Public Education Workshop
16

## Slide 17
PART 1 — THE COMPACT
Conditional Removal & Curie Release Letters
Conditional Removal Letter
Required by some agreements before waste may be imported
Written request submitted by the agreement holder to Commission administration
Needed if waste comes from another compact requiring export authorization, or from the Northwest Compact
Needed if a broker, processor, or collector must obtain generator and/or export authorizations first
Curie Release Letter
Required when an agreement requests more than 15,000 curies
Contingent on availability under the 275,000-curie fiscal-year cap set by the Legislature
Agreement holders must request in writing at least 15 days before shipment
TLLRWDCC Public Education Workshop
17

## Slide 18
PART 2 — GENERATORS & BROKERS • NEW TOPIC
Who Is the “Last Beneficial User”?
The Commission's view of who a “generator” is centers on the last beneficial user — the entity that actually used the material for its intended purpose before it became waste.
Brokers
Are not the last beneficial user
Processors
Are not the last beneficial user (some exceptions)
Recyclers
Are not the last beneficial user
Status-changer
The entity that changes an item from “licensed radioactive material” to “low-level radioactive waste” may or may not be the last beneficial user
TLLRWDCC Public Education Workshop
18
The Commission ensures the CERCLA process for generator attribution maintains integrity through the process.

## Slide 19
PART 2 — GENERATORS & BROKERS
Brokers, Processors & Recyclers
Why Brokers Matter
Thousands of entities nationwide hold radioactive materials
Many lack the expertise to package, classify, and ship waste to State, NRC, DOT, and WCS WAC standards
Yet their LLRW must still be disposed of safely and properly
Brokers help ensure safe, compliant, and often more economical disposal
Beyond Disposal
Recyclers: give sealed sources with remaining useful life a pathway other than disposal — function somewhat like brokers
Waste processors: assist with volume reduction and changes to waste form; may also act as a broker
Storage services are also available
TLLRWDCC Public Education Workshop
19

## Slide 20
PART 2 — GENERATORS & BROKERS • NEW TOPIC
Self-Generated Waste by Brokers & Processors
Brokers and processors don't generally generate LLRW themselves — so when they do, the Commission asks for a detailed explanation.
Because brokers and processors are not typically “generators,” self-generated waste is the exception, not the rule
A detailed explanation is required to document how and why the waste was generated
This keeps waste attribution clear for any future concern or need — protecting the integrity of the last-beneficial-user framework
TLLRWDCC Public Education Workshop
20

## Slide 21
PART 2 — GENERATORS & BROKERS • NEW TOPIC
International Waste
Import applications must certify the waste proposed for importation is not waste of international origin.
How Origin Is Decided
Acceptance is not based on which country “provided” the material
It's based on which company or entity owned and had last beneficial use of the source
The Commission does not generally consider where americium was manufactured
In Practice
U.S. Government waste may be disposed of at the CWF regardless of generation location, if it meets classification, Waste Acceptance Criteria, and TCEQ approval requirements
The Commission has, on multiple occasions, rejected waste that could have been generated internationally
TLLRWDCC Public Education Workshop
21

## Slide 22
PART 2 — GENERATORS & BROKERS
OSRP & SCATR Programs
OSRP (DOE)
Focused on very high-activity sources — primarily cesium and cobalt
DOE takes ownership at the generator site
Generally not disposable at the CWF
SCATR (DOE)
Typically administered through the CRCPD
A contracted broker takes and disposes of sealed sources across many radioisotopes and activities
DOE pays a portion of the disposal cost
The Southeast Compact also runs a similar program
TLLRWDCC Public Education Workshop
22

## Slide 23
Questions?
tllrwdcc.org
Stephen Raines, Executive Director
512-350-6241 • stephen.raines@tllrwdcc.org